## Slide 1: Crowbar Circuit
Assignment 5.2
By: Matthew Sender

## Slide 2: Function
Prevent reverse polarity
Prevents overloads
Uses a sacrificial fuse
Low current draw
Notes: The crowbar circuit can be used to protect the circuit from an overload of power as well as protect the circuit from getting positive and negative reversed. It protects from reverse polarity by using a fuse of some type, whether it is a built-in resettable fuse or a fuse that the consumer can replace themselves. The power goes through the fuse into the circuit like normal except right after the fuse you put a polarized diode with the cathode on the positive side and then the anode to ground. Placing the diode in this configuration results in minimal power consumption when the correct polarity is being used on the circuit. However, when reversed polarity is applied to the circuit it shorts to ground through the diode causing a large amount of current flow. The large amount of current flow then trips or burns out the fuse depending on the type of fuse used. The crowbar circuit can protect all your hard work from burning out.

## Slide 3: Uses
Prevents accidentally reversal of polarization
Prevents overload of power
Notes: There are a few uses for a crowbar circuit, it can protect a circuit from being overloaded by power. It can also be used to prevent reverse polarity from occurring in a circuit. There are many applications for the crowbar circuit, one being power supplies the crowbar circuit protects the more expensive components by “dropping a crowbar” across the bus bar. Using the crowbar circuit in this fashion protects the user and their projects as well as the power supply from damage by overload or shorting. Since it drops the metaphorical crowbar on the bus of the power supply it shorts the circuit causing higher amperage than the fuse can handle thus blowing it and saving the consumer and protecting the power supply. This will allow the user to only replace the built-in fuse or the replaceable fuse for the circuit to work again. The crowbar circuit can be useful in several situations to protect your supplies if you make a mistake.

## Slide 4: Advantages
Lower power consumption
Easy to execute
Cheap
Notes: The advantages of the Crowbar Circuit that it has a lower power consumption, it’s easy to execute, and that it’s cheap. It has lower power consumption because it doesn’t get used until the failsafe kicks in. Therefore, it doesn’t much take away from the power that is going to the rest of your project. The diode doesn’t allow the current to go in until the polarity is reversed. This is easy to execute because it only involves two components: a fuse and a diode. There are several different types of fuses that you can use, so you do not need a specific kind of fuse. You can also purchase a diode for very cheap as well. Overall, this circuit is one that is worth incorporating into your projects, because it is cheap, easy to execute, and it doesn’t consume a lot of power. It seems to be an easy enough way to protect your work.

## Slide 5: Disadvantages
Dependent upon Zener voltage value
Subject to noise problems
Fuse requires help after blowing
Fuse needs to be replaced
Notes: While the Crowbar Circuit seems to be beneficial in many ways, it also has its disadvantages. The overvoltage value depends on the Zener diode voltage value, the circuit is subject to noise issues, and the fuse requires manual help after blowing and needs to be replaced. When you create your crowbar circuit, the value of the diode that you use depends on the overvoltage value that triggers the failsafe. The circuit is also subject to noise problems. Loud noises could trigger failure and blow the fuse prematurely. After the fuse blows, the circuit needs manual help to run. The average consumer may not be able to help the circuit. Lastly, after the fuse is blown, it needs to be replaced. This means time, energy, and money spent replacing the fuse. Overall, if you are knowledgeable about the circuits and know how to run and replace the fuses, this may be a helpful circuit for you.

## Slide 6: Variations
Triac and SSB
Triac and Zener
SCR
Notes: There are three main types of Crowbar circuits: using Triac and SSB, Triac and Zener Diode, and using SCR. The Triac and SSB variation uses an SSB or a silicon bilateral switch as the trigger to activate the triac. The triac is being used as a gate between the power and ground. The voltage trigger point is determined by the resistor that is attached to the SSB. Using Triac and Zener Diode is similar, but using the Zener Diode instead of the SSB. The Zener voltage would decide the trigger point of the crowbar circuit. With this variety, you don’t need to have a resistor to set the limit, the diode does it itself. This way is less complicated than others. The last variety is using an SCR transistor, this is very similar to the previous version, but it uses the SCR around the regulator circuit to prevent damage to it when the triac is tripped. The SCR is activated by the Zener diode, which switches on the triac. When the Triac is switched on, the system is shorted.

## Slide 7: References
Reverse Polarity Protection. 3rd Planet Solar / KC9ON. (2020, October 7). https://kc9on.com/ham-radio/station-accessories/reverse-polarity-protection/#:~:text=The%20crowbar%20works%20by%20putting,causing%20the%20fuse%20to%20blow.
Practical Electronics/Crowbar Circuit. Wikibooks, open books for an open world. (n.d.). https://en.wikibooks.org/wiki/Practical_Electronics/Crowbar_circuit
Fmuser FM/TV broadcast one-stop supplier. (n.d.). https://fmuser.net/